## Slide 1
AssertionForge
LLM-Driven SystemVerilog Assertion Generation
for Formal Verification
Group 2 · CS525 – Formal Methods for System Verification Pranjal · Dhruvkumar R Pansuriya · Shrish Uttarwar
IIT Guwahati · Dept. of Computer Science & Engineering · April 2026

## Slide 2
Agenda
2 / 25
01
Abstract & Motivation
02
Introduction & Problem Statement
03
Related Work
04
System Architecture Overview
05
Stage 1 – Knowledge Graph Construction
06
Signal Mapping (Spec↔RTL Alignment)
07
Stage 2 – Multi-Resolution Context Synthesis
08
Stage 3 – SVA Generation
09
Addressing Core Challenges (P1–P5)
10
Stage 4 – Quality Gating & Verible
11
Multiagent + GPTCache Architecture
12
Results, Limitations & Future Work

## Slide 3
Abstract
3 / 25
Core Objective
Automate SystemVerilog Assertion (SVA) generation from natural-language specifications and RTL code using LLMs — improving correctness, explainability, and cloud efficiency.
Five Core Challenges Addressed:
P1
Long-Context Limits
P2
Agent Memory
P3
Cloud Efficiency
P4
Redundancy
P5
Feedback Refinement
Outcome: A modular pipeline — KG construction · signal mapping · context retrieval · prompt compression · multiagent caching · SVA validation

## Slide 4
Introduction & Motivation
4 / 25
The Core Bottleneck
Writing SVAs requires simultaneously understanding multi-page natural-language specifications AND thousands of lines of RTL code.
Existing LLM methods operate in isolation — missing implementation details or lacking behavioral context.
Natural Language
Specification
100s of pages
▶
RTL Code
(Verilog)
1000s of lines
▶
LLM Pipeline
(Our System)
AssertionForge
▶
Formal SVAs
Correct & Verified
Research Question:
How can an automated system synthesise information from ambiguous multi-page specs and complex RTL
to generate SVAs that are both syntactically correct and semantically meaningful — within token and cost limits?

## Slide 5
Related Work
5 / 25
AssertLLM
• End-to-end SVA generation from NL specs (3 stages: extraction → signal mapping → synthesis)
• Limitation: operates on spec only, misses RTL implementation details
• Our extension: joint spec + RTL reasoning
ClarifyGPT
• Detects ambiguous prompts via consistency checks across multiple generated outputs
• Triggers targeted clarification when inputs are insufficient
• Inspires our KG density threshold for 'context gap' detection
STELLAR
• Structure-aware retrieval using AST structural fingerprints
• Retrieves similar (RTL, SVA) pairs as few-shot prompts
• Inspires our structural retrieval module for sparse KG neighbourhoods

## Slide 6
System Architecture — Full Pipeline
6 / 25
Stage 1
Extraction &
Alignment
▶
Stage 2
Context Synthesis
& Compression
▶
Stage 3
Multi-Agent
Generation
▶
Stage 4
Checking
& Repair
Spec PDF +
RTL Verilog
GraphRAG KG
(Spec-side)
PyVerilog
(RTL-side)
Signal Mapping
& Alias Table
Unified KG
G = (V, E)
Global
Summarisation
Signal-Specific
Retrieval (SSR)
GRW-AS
Random Walk
LLMLingua
Compression
GPTCache
Routing
Agent C
NL Test Plan
Agent D
SVA Synthesis
Gemini API
(Deep Reasoning)
Groq API
(Fast Format)
Cache
Deduplication
Phase 1
Alias Validation
Phase 2
Verible Syntax
LLM Repair
Loop
Accepted SVAs
.sva files
Diagnostics
JSON Reports

## Slide 7
Stage 1 — Knowledge Graph Construction
7 / 25
Spec-Side: GraphRAG + Domain Schema
Entity Types (Et):
Module · Signal · Port · Register · FIFO · Clock · Interrupt · FSM · Protocol · Constraint
Relation Types (Rt):
connectsTo · defines · triggers · dependsOn · HasSignal · UsesClock · DescribesOperation · transmitsData
Schema semi-automatically discovered via LLM → human expert merges redundant concepts
RTL-Side: PyVerilog Parser
Module structure — AST traversal; ports (direction, width); module instantiations
Signals & assignments — continuous (assign) and procedural (always-block); LHS targets & RHS deps
FSM detection — always-blocks + case statements; state variables matched via naming patterns
Dataflow analysis — VerilogDataflowAnalyzer builds binding graph via getBindings()
KG refinement — RTL info merged into G₀ to enrich spec-side graph
Spec KG + RTL KG → Unified Knowledge Graph G = (V, E)
Spec KG + RTL KG → Unified Knowledge Graph G = (V, E)

## Slide 8
Signal Mapping — Bridging Spec & RTL
8 / 25
"system reset" in spec ↔ nRST / rst_n in RTL — without alignment, generated SVAs reference non-existent signals
1
Input Extraction
Spec entities from KG node types (SIGNAL, PORT, REGISTER, CLOCK)
RTL module ports & internal signals from PyVerilog
2
LLM Semantic Alignment
LLM receives mentions + RTL signals + local spec context
Outputs JSON: canonical_name · rtl_name · confidence · active_low · match_method
3
Alias Table Construction
Fast lookup: RTL signal → canonical name
Normalises naming variants; basis for fuzzy fallback matching
4
Confidence Gating (≥ 0.7)
HIGH: inject corresponds_to edges into Unified KG
LOW: string-based substring similarity → references edges
Key Artifacts
▸ signal_aliases.json
▸ alias_lookup_table.json
▸ signal_mapping_decisions.json
▸ alignment_full_prompt.txt
▸ signal_mapping_overview.json

## Slide 9
Stage 2 — Multi-Resolution Context Synthesis
9 / 25
For each target signal v
i
∈ V, up to B=3 distinct prompts are constructed from three generators:
(i)
Global Summarisation
LLM generates 5 complementary summaries of full spec + RTL:
• High-level design overview • RTL architecture summary
• Per-signal summary • Design patterns (FSMs, pipelines)
• Signal-specific description for vᵢ ➝ Generated once, cached across all signals
(ii)
Signal-Specific Retrieval (SSR)
Hybrid retriever: TF-IDF (sparse) + Sentence Transformer (dense)
5 granularity levels: 50 · 100 · 200 · 800 · 3200 tokens
Overlap ratios 0.2 & 0.4 → Top 20 chunks ranked by cosine similarity
(iii)
GRW-AS — Guided Random Walk with Adaptive Sampling
Novel contribution: 70 biased random walks × 100-step budget from vᵢ
Path → natural language: 'A drives B, part of module C, involving verification point D'
LLM-as-Pruner scores SSR ∪ GRW-AS on relevance + density + diversity → retains optimal subset
Why KG beats flat RAG: Cross-document traceability · Causal chain discovery · Compression resistance

## Slide 10
Stage 3 — SVA Generation
10 / 25
Two-Step Generation via GPT-4o
Step 1
Natural Language Test Plan
LLM generates human-readable verification intents from pruned context
e.g. "Verify that TX_EMPTY asserts when the FIFO count reaches zero"
→ nl_plans.txt
Step 2
SVA Synthesis
Each NL plan → formal SystemVerilog Assertion
Prompt includes correct SVA syntax examples as few-shot guidance
e.g. @(posedge PCLK) ((PADDR >= 24) && (PADDR <= 31)) && (PENABLE) |-> ((PADDR >= 0) ...
→ property_goldmine_N.sva
Output artifacts: nl_plans.txt · sva_details.csv · generated .sva files under run tbs/

## Slide 11
KG as Robust Agent Memory (P2)
11 / 25
Traditional RAG fails when causal hardware logic is fragmented across semantic chunks.
RQ1.4
Memory Representation & Fidelity
Structured entity-relation schemas (E_t, R_t) outperform flat embeddings.
KG enforces relational memory — updates are edge insertions/attribute changes, not vector dilution.
Causal links (clock-domain crossings, nested resets) preserved reliably.
RQ1.6
Task-Adaptive Memory Granularity
Broad Test Planning (Agent C): coarse-grained SSR at 800+ token chunks.
Precise SVA Synthesis (Agent D): GRW-AS extracts exact causal chains (TX_EMPTY → apb → PRESETn).
LLMLingua applies high compression to verbose spec memory, keeps RTL memory intact.
Memory structure: Spec Vectors (semantic) + RTL AST (structural) → fused inside Unified KG

## Slide 12
The Missing Context Problem (P1) — Root Cause Analysis
12 / 25
When a signal's KG neighbourhood is sparse → SVAs pass syntax but fail functionally (LLM lacks behavioral constraints).
Cause A: KG Extraction
Failure
Behavior exists in RTL but GraphRAG failed to extract its relationships from NL text → artificially sparse KG neighbourhood.
Cause B: Specification
Incompleteness
NL document is flawed — behavioral rules or edge-cases for the target signal are simply not documented. No retrieval can find what isn't written.
Cause C: Structural Blindness
of Retrieval
Semantic / keyword search finds the signal name but misses the underlying control flow (nested if-else, FSM transitions, clock-domain crossings) governing actual hardware behavior.
Deterministic Fallback Approaches:
RTL Program Slicing
Backward slice from target signal → deterministic structural context; resolves Cause C
STELLAR AST Retrieval
Structural fingerprints retrieve similar (RTL, SVA) pairs as few-shot prompts; resolves Causes A & B

## Slide 13
LLMLingua — Prompt Compression (P1 + P3)
13 / 25
Coarse-to-fine prompt compression: small LM computes token perplexity → prunes low-information tokens → compressed prompt to GPT-4o / Groq.
① Budget Controller
Allocates different compression ratios to instructions, demonstrations & questions
② ITPC Algorithm
Iterative Token-Level Prompt Compression — models inter-token dependencies during pruning
③ Distribution Alignment
Fine-tunes small model to approximate target LLM's distribution; preserves semantic integrity
Dynamic Budget Strategy (Hardware-Tuned):
LOW Compression (Keep 70–80%)
GRW-AS KG paths · RTL backward slices · STELLAR examples
→ dense, structurally rigid, critical causal logic
HIGH Compression (Keep 35–40%)
Raw SSR text chunks from spec PDF
→ verbose, redundant, recovers well under perplexity-based compression
Result: 4616 → 3876 tokens · 16.03% reduction · NL Generation: 2163→1807 · SVA Generation: 2453→2069

## Slide 14
GPTCache — Semantic Caching Layer (P3 + P4)
14 / 25
Eliminates redundant cloud API calls by storing and retrieving semantically similar prompt responses.
Query
+Prompt
→
Embedding
Generator
→
Similarity
Evaluator
→
Cache
Hit?
YES →
Return Cached
Response (0ms)
NO ↓
Call
Cloud LLM
→ Store → Return
Problems Addressed:
RQ1.7 — Minimizes information transfer; cached responses bypass full prompt re-transmission
RQ2.2 — Early redundancy detection; intercepts repeated queries before reaching LLM
RQ2.4 — Prompt mapping via embedding-based similarity; reuses results above threshold
RQ2.5 — Flexible caching granularity: prompt-level or chunk-level
Cache key = hash(agent_id + prompt_version + exact context) → prevents cross-agent contamination

## Slide 15
Stage 4 — Verible Syntax Validation & Repair (P5)
15 / 25
Feedback-driven refinement loop using Verible — SystemVerilog-aware syntax checker.
Feedback Signals (RQ3.1):
Binary: SVA passes / fails syntax check (#SynC)
Structured: Verible stderr — precise diagnostics (e.g., missing clocking event, invalid operator)
Localized: Line-level error → identifies exact failing assertion fragment
Repair Loop (RQ3.2):
Generate SVA
from LLM
→
Wrap in minimal
SV module
→
Run Verible
syntax check
→
Errors?
Extract snippet
→
Build repair
prompt
→
Re-invoke LLM
→ corrected SVA
Safeguards (RQ3.3):
Local correction per-instance · Bounded repair iterations · Context preserved across iterations · Syntax decoupled from semantic generation

## Slide 16
Two-Phase Assertion Quality Gate (TC3)
16 / 25
Standalone batch filter — intentionally decoupled from main pipeline for independent reuse.
Phase 1 (Loop A)
Semantic Alias Validation
[ Disabled by default (--enable-loop-a) ]
Extract candidate identifiers from SVA
Compare with valid alias lookup table
One repair attempt if invalid signals detected
Why default-off: strict pre-filter over-rejects on noisy/generated corpora
Phase 2 (Loop B)
Verible Syntax Check
[ Default active mode ]
Wrap assertion in minimal valid SV module using RTL signals
Run verible-verilog-syntax binary
One repair attempt on failure
Verible resolved via: --verible-bin → PATH → .tools/verible/**/bin/
Outputs: accepted/ · discarded/ · reports/summary.json · reports/detailed_results.json · reports/logs/

## Slide 17
Multiagent Orchestration with GPTCache
17 / 25
Task decomposition + specialisation to improve assertion quality while maintaining cloud efficiency.
Agent A
Spec
Understanding
→Gemini
Agent B
RTL
Grounding
→Gemini
Agent C
Test
Planner
→Groq
Agent D
SVA
Synthesizer
→Groq
Agent E
Referee /
Checker
→Gemini
Shared GPTCache — key = hash(agent_id + prompt_version + context)
Cache HIT → 0ms response · Cache MISS → route to Gemini (deep reasoning) or Groq (fast formatting)
Gemini API
Agents A & E — deep reasoning, large context windows
Groq API
Agents C & D — high-speed, structured formatting & repair
Response envelope tracks: content · model_name · cache_hit · latency_ms · token_usage

## Slide 18
Agent Specialisation Roles
18 / 25
Agent
A
Spec Understanding
Extracts requirement-level semantics, constraints & edge-case behavior from natural language specification.
Agent
B
RTL Grounding
Maps textual semantics directly to structural RTL nodes and parsed signals — integrates the Signal Mapping pipeline.
Agent
C
Assertion Planner
Converts grounded requirements into human-readable, test-plan style verification intents (NL plans).
Agent
D
SVA Synthesizer & Repair
Generates formal SystemVerilog Assertion syntax and iteratively repairs it based on Verible compiler feedback.
Agent
E
Referee / Consistency Checker
Cross-checks final syntactically valid SVAs against original specification intent — prevents over-constraining.
All agents share one GPTCache → deduplication across specialisations → no redundant cloud calls

## Slide 19
Implementation Highlights
19 / 25
🔁
Migration: OpenAI → Groq API
Decoupled tightly-coupled OpenAI backend; cost-effective inference without compromising output quality.
⚙️
Custom Design Tested End-to-End
Full pipeline executed on custom APB peripheral hardware (UART/SPI with APB interface). SVAs generated for PCLK, PRESETn, PADDR, PSEL, PENABLE, PWRITE, PWDATA, PRDATA, PREADY, PSLVERR.
🗂️
GraphRAG with Hardware Schema
Replaced generic entity-extraction with hardware-specific schema Σ = (Et, Rt); 14 entity types, 10+ relation types; human expert merges redundant concepts.
✅
Local Verible Binary Resolution
Robust priority chain: --verible-bin → PATH → .tools/verible/**/bin/ — eliminates 'not found in PATH' errors on constrained machines.
📋
Deep Traceability
Prompt snapshots · raw model responses · mapping decisions · run-level & per-iteration quality logs · structured result JSONs — auditable, reproducible workflow.

## Slide 20
Addressing Core Challenges — P1 to P5 Summary
20 / 25
P1
Long-Context Limits
KG node-to-node linking reduces irrelevant chunks · SSR multi-resolution retrieval · LLMLingua minimal context selection (RQ1.1)
P2
Agent Memory
Unified KG as persistent cross-domain memory · structured relational schema vs flat embeddings · causal chains preserved (RQ1.4, RQ1.6)
P3
Cloud Communication Efficiency
LLMLingua: 16% token reduction · GPTCache eliminates redundant API calls · Groq for fast-turnaround agents (RQ1.7, RQ1.8)
P4
Redundancy in Multi-Agent Systems
Signal mapping encoded once in KG — reused across all assertion generations · GPTCache: early redundancy detection across agents (RQ2.2)
P5
Feedback-Driven Refinement
Verible closed-loop repair: binary + structured + localised error signals · bounded iterations · context preserved · syntax decoupled from semantics (RQ3.1–3.3)

## Slide 21
Results & Evaluation
21 / 25
Key Observed Outcomes from End-to-End Execution
16%
Token Reduction
via LLMLingua
25+
SVA Files
processed (TC3)
100%
Syntax-Valid
accepted (Verible-only)
0.7
Confidence
Threshold (Mapping)
Qualitative Findings:
Signal mapping LLM produced high-accuracy alignments (confidence 1.0 for clear signals like PERIPHERAL SELECT → sdc_top.psel)
Graph connectivity directly dictates retrieval quality — missing edges degrade SVA accuracy
Edge creation is brittle: hard edges depend on strict string matching with spec node names; fuzzy fallback is essential
Verible-only default (Loop A disabled) was optimal for noisy/generated SVA corpora — strict alias pre-filter over-rejects
LLMLingua compression is safe for structured RTL content; spec prose compresses aggressively without quality loss

## Slide 22
Traceability & Reproducibility
22 / 25
Every run is fully auditable — diagnostics treated as first-class artifacts.
Prompt Traces
▸ alignment_system_prompt.txt
▸ alignment_user_prompt.txt
▸ alignment_full_prompt.txt
▸ alignment_raw_response.txt
Signal Mapping
▸ spec_entities.json
▸ rtl_signals.json
▸ signal_aliases.json
▸ signal_mapping_decisions.json
▸ signal_mapping_overview.json
Generation Outputs
▸ nl_plans.txt
▸ sva_details.csv
▸ property_goldmine_N.sva
▸ alignment_input_bundle.json
▸ alias_lookup_table.json
Quality Reports
▸ reports/summary.json
▸ reports/detailed_results.json
▸ reports/summary.txt
▸ reports/logs/run_*.log
▸ reports/logs/iterations/*.log

## Slide 23
Limitations & Known Gaps
23 / 25
L1
Multiagent Controller Not Fully Production-Ready
Full end-to-end multiagent orchestration with shared GPTCache is architecturally designed and partially scaffolded — not yet a single unified production controller.
L2
Repair Function Currently Stubbed
repair_sva_with_llm(...) in the standalone TC3 checker returns the original SVA unchanged. Interface is ready; real LLM repair integration is pending.
L3
Alias-Based Loop A Sensitivity
Strict signal validation (Loop A) may need stronger token-cleaning for noisy/generated SVAs — currently disabled by default to avoid over-rejection.
L4
Signal Edge Materialization Fragility
Creating hard corresponds_to edges depends on strict string matching between LLM-produced names and KG spec nodes. Naming mismatches reduce graph connectivity.
L5
No Semantic/Formal Validation Stage
Quality gate stops at syntax (Verible). Functional correctness under formal verification (e.g., via SymbiYosys / JasperGold) is not yet automated in the pipeline.

## Slide 24
Future Work
24 / 25
🔧
Real LLM Repair Integration
Implement repair_sva_with_llm() with schema-constrained JSON output for systematic, parseable fix generation.
🧪
Semantic & Formal Validation Stage
Add post-syntax validation: property equivalence checks, formal model-checking hooks (SymbiYosys), functional correctness beyond Verible.
🔗
Robust Signal Edge Materialization
Improve mention-matching robustness (fuzzy + semantic + edit-distance) for reliable corresponds_to edge creation even with naming noise.
🚀
Production Multiagent Controller
Complete the unified multiagent orchestration layer with GPTCache telemetry dashboard — latency, cache hit ratio, token savings per agent.
📊
Benchmark Suite
Quantitative evaluation: cost/latency/acceptance with vs without cache & multiagent; SVA correctness (#SynC, #SemC) across real-world hardware designs.

## Slide 25
Conclusion
◆ AssertionForge combines graph-grounded LLM generation with robust post-generation validation
◆ Semantic signal mapping bridges Spec ↔ RTL — eliminating hallucinated signal references
◆ Multi-resolution retrieval (SSR + GRW-AS) surfaces causal hardware logic invisible to flat RAG
◆ LLMLingua + GPTCache jointly reduce token usage and redundant API cost across agents
◆ Verible-backed two-phase quality gate provides automated, closed-loop syntactic refinement
◆ Proposed multiagent architecture (Agents A–E) enables specialised, scalable SVA synthesis
CS525 – Formal Methods for System Verification · Group 2 · IIT Guwahati · April 2026